## Slide 1
Industrial Minerals and Rocks

## Slide 2
Definitions :
Economic geology is one of Geology (Earth sciences) branches, which is concerned with earth’s crust or Lithosphere materials that can be used for economic or industrial purposes. These materials called economic resources, which include; metals (like gold, &platinum), nonmetallic minerals (like sulphur & graphite), industrial minerals & rocks (like limestone, claystone & gypsum) which is used in manufacture of (cement, ceramic, lime, & glass), energy resources or fuels (petroleum, coal, & natural gas) and water.

## Slide 3
With the exception of water these resources are called Economic minerals, they are an accumulation of minerals having economic value for the benefit of mankind, which are concentrated in sufficient quantity as to be capable of economic extraction. Different economic minerals presents as mineral deposits in earth’s crust, they are concentrated accumulations of ore minerals and industrial minerals and rocks.

## Slide 4
The elements that enter into the mineral deposits have been derived either from the rocks of the earth’s crust and upper mantle or magma. 99 % of the earth’s crust is made up of major elements (O, Si, Al, Fe, Ca, Na, K, Mg, & Ti), many other elements are 1 %. So geologic processes must concentrate these elements hundreds to thousands of times to make ore deposit.

## Slide 5
Classification of economic minerals about using as raw materials for the different industries (Gregory, 1980):
1- Metallic minerals (minerals that yield metals):
Precious metals: gold, silver, platinum
Base metals: copper, lead, zinc, tin
Steel industry metals: iron, nickel, chromium, manganese, molybdenum, tungsten, vanadium
Light metals: aluminum, magnesium
Electronic industry metals: cadmium, bismuth, germanium
Radioactive metals: uranium, radium

## Slide 6
2- Nonmetallic minerals:
Insulating materials: mica, asbestos
Refractory materials: silica, alumina, zircon, graphite
Abrasives and gems: corundum, emery, garnet, diamond, topaz, emerald, sapphire
General industrial minerals: phosphate rock, rock salt, limestone, barite, borates, feldspars, gypsum, potash, clays, magnesite, sulphur

## Slide 7
3- Fuel minerals:
Solid fuels: anthracite, coal, lignite, oil shale
Fluid fuels: petroleum oil, natural gas
With the exception of Fuel minerals, and Metallic minerals (ores geology), so the term nonmetallic minerals is brief and convenient, it is used to comparison with metallic minerals. But the expression industrial minerals and rocks is more accurate and descriptive. It indicates both a natural industrial minerals & rocks, and manufacturing product materials.