## Slide 1
Exploration stages of Economic minerals deposits (nonmetallic ores):
The mineral deposits ores can be described as concentrated accumulations of ore minerals or industrial minerals and rocks in sufficient quantity as to be capable of economic extraction.
The exploration of mineral deposits falls into four stages:
1- Locate the deposits and geological studies.
2- Evaluation of mineral deposits and Estimation of their reserve, then studying the Technical and Economic Feasibility of exploitation these deposits.
3- Mining and Extraction (open-pit & underground mining methods).
4- Processing of treatment and beneficiation.

## Slide 2
Mining operations:
Minerals may be mined and processed for more than one purpose. The mineral may be a metal ore, when it is used to prepare the metal, as when bauxite (hydrated aluminium oxide) is used to make aluminium. The mineral is classified as a nonmetallic ore when bauxite is used to make material for refractory bricks or abrasives.
Mining is the process of extracting minerals of economic value from the earth’s crust for the benefit of mankind.
A mine is an excavation made in the earth for the purpose of extracting useful minerals.

## Slide 3
The four main classes of mining operations (Gregory, 1980):
1- Underground mining: (ore is far from surface & the covered rocks are hard & thick)
Near vertical vein deposits,
Horizontal bedded deposits (metals, nonmetals)
2- Surface (open-pit) mining: (ore is near from surface, the covered rocks are soft & thin)
Quarrying of construction (building) stones
Mining of metals & nonmetals

## Slide 4
3- Alluvial mining: (for alluvial deposits & heavy minerals)
Beach dunes, Stream beds & terraces
4- Non-entry mining:
Solution mining of copper
Frasch process for sulphur
Oil wells (petroleum, natural gas, water)