## Slide 1
Building and Construction materials:
Aggregates:
It is a mixture of rocks fragments. Aggregate comprise 3/4 volume of concrete
(85-90% aggregate and 10-15% cement) and have physical, mechanical, thermal, and chemical properties.

## Slide 2
Aggregates classify according to source to:
1- Natural aggregates (sand and gravel): it is extracted from quarries, which was formed by disintegration of rocks (igneous, sedimentary, & metamorphic) through weathering, erosion, transportation of fragments by (air, water, & glacier) & deposition.
2- Artificial aggregates (slag, crushed stone): it is formed by:
1- By-product (blast furnace slag, fly ash, burned rocks)
2- Thermal process (fired clay, vermiculite)
3- Recycled concrete and municipal wastes

## Slide 3
Natural aggregates classify according to particles shape about BS 812 / 1975 to:
1- Rounded 2- Irregular 3- Flaky 4- Angular 5- Elongated 6- Flaky & Elongated
Natural aggregates classify according to surface texture of grains about BS 812:1975 to:
1- Glassy (flint) 2- Smooth (chert) 3- Granular (sandstone) 4- Rough (basalt)
5- Crystalline (granite) 6- Porous (pumice)

## Slide 4
Natural aggregates classify about grain size according to classification of Wentworth scale and British institute of geological science to:
1- Grains size > 4mm are called gravel (pebbles, copples, boulders) composed of rock fragments.
2- Grains size 4 - 0.063 mm are called sand composed mostly of quartz.
3- Grains size < 1/16 or 0.063 mm known as fines consist of silt and clay fractions.