## Slide 1
Geological forms (occurrence) of sand & gravel deposits:
1- | River deposits (main source in Iraq) | 
2- | Glacial deposits | 
3- | Terrace deposits | un consolidation deposits
4- | Continental shelf deposits | 
5- | Aeolian deposits (sand dunes) | 
6- | Beach deposits | 
7- Lithified (solid deposits) beds or lenses like present in Injana Formation (Miocene age).
Pliocene and Pleistocene (Quaternary) deposits cover vast areas of Iraq, underlying Mukdadiya and BaiHassan Formation (Pliocene).

## Slide 2
Uses of sand and gravel :
1- Concrete & mortar
2- Filling & grouting
3- Road pavement & railway road ballast
4- Concrete products (Pipes, Blocks, Tiles, Thermstone, Kerbstone, and Lime-Sand brick)
5- Water purification filters
6- Glass, Refractory, Foundry & Ceramic
7- Manufacture of Portland cement

## Slide 3
Evaluation the natural sources aggregate using for concrete and building according to
Iraqi standard specification (IQS) no. 45/1984:
1- Sieving and grading:
Grain size distribution is termed grading. Grading must be well graded, not have one size. The constant grading increases the pores, so results a lessening in strength of concrete. The grain size of aggregate varies depending on the use of aggregate .

## Slide 4
IQS no. 45/1984 classify Natural aggregates according to grain size to:
1- Fine aggregate (sand): grain size < 5mm or passing from sieve no. 4
2- Coarse aggregate (gravel): grain size > 5mm or retained on sieve no. 4
3- Total aggregate: mixture of the two sizes

## Slide 5
Fine materials consist of silt & clay fractions or passing from sieve no. 200 (0.075mm). Upper limit of fine materials is 5% for fine aggregate, & 3% for coarse aggregate. Fine materials usually comprise < 10% of total volume of aggregate, so need to be reduced to < 5% by washing and sieving.