## Slide 1
Some Basic Definition
Ore–body: A more or less solid mass of ore that may consist of low-grade as well as high-grade ore of known dimensions and that is of different character from the adjoining rock and can be extracted at a profit.
Ore lode: Is a deposit of metalliferous ore that fills or is embedded in a fissure (or crack) in a rock formation or a vein of ore that is deposited or embedded between layers of rock.

## Slide 2
Ore shoot: A large and visually rich aggregation of ore minerals having an elongated vertical zone of pipe-like, ribbon-like or chimney like shape within a deposit (usually vein).
Syngenetic ore: refers to ore deposits that form at the same time as their host rocks.
Epigenetic ore: refers to ore deposits form after their host rocks.
Hypogene ore: refers to mineralization caused by ascending hydrothermal solutions.
Supergene ore: refers to mineralization caused by descending solutions.

## Slide 3
Ore Reserve:
The amount of the metal present in an economical minable part of the discovered ore after appropriate assessments and studies that have been carried out to delineate the ore boundaries that can be extracted at a profit after consideration of all factors affecting the value of the cut-off grade.
Ore reserves are classified with respect to the confidence level of the estimate that increases with the increased level of geological knowledge during mine development. Traditionally, ore reserves have been classified as proven (measured), probable (indicated), possible, and inferred (See Fig 1).

## Slide 4
Ore reserve types :
Proved Ore Reserves: It is the amount of metal contained in the economically mineable part of a measured ore. A proved ore reserve represents the highest confidence category of reserve estimate. Proven ore has been regarded as that which is "blocked out" (measured, sampled, and assayed on four sides).

## Slide 5
2. Probable Ore Reserves: It is the amount of metal present in the economically mineable part of an Indicated ore. A probable ore reserve has a lower level of confidence than a proved ore reserve but is of sufficient quality to serve as the basis for decision on the development of deposit. In this case the style of mineralization and other factors do not permit achievement of proved reserve. Probable ore as blocked on three sides.
3. Possible Ore Reserve: as blocked on two sides.