## Slide 1
Movement of magma and magmatic fluids
Magma and magmatic fluids transported by the following ways acting singly or together:
1- mechanical pressure
2-tectonic stress or compression
3- movement of gases
4- magmatic assimilation
5- magmatic stoping

## Slide 2
Modes of ore minerals crystallization :
Concentration and Crystallization of the metallic minerals from magma and magmatic fluids by:
1- Direct crystallization from magma
2- Magmatic differentiation

## Slide 3
2- Magmatic differentiation:-
(a) Partial fractionation
(b) Differentiation by gravity
Settling of crystals in a magma chamber can concentrate minerals like :- Spinel Group of Minerals all relatively dense. spinel: MgAl2O4
Basaltic magmas contain about: 10% Fe , a few percent Ti and trace amounts of Cr, Mn, and V
Under favorable circumstances these become concentrated in the spinel. Since the spinel crystals are dense, they can sink to the bottom of a slowly cooling magma body and make layers of ore
Density of basaltic magma: 2500 kg/m3
Density of Cr spinel: 4800 kg/m3

## Slide 4
(C) Magmatic fluids immiscibility
Oil and water don’t mix . As magmas cool, they can split into two liquids of different composition and density. One of these liquids is the silica-rich melt, It has the most volume and the other, typically much smaller in volume, can be rich in metal oxides, sulfides or carbonate. Desirable element is preferentially concentrated into the low-volume melt.

## Slide 5
Types of Immiscible Melts
Oxide melts can be rich in Fe (Fe2O3, hematite) and Ti (FeTiO3, ilmenite).
Sulfide melts can be rich in Ni, Cu, and the platinum-group elements, in addition to iron sulfur (FeS, pyrrhotite).
Carbonate melts can be rich in niobium, tantalum, rare earths, copper, thorium, and phosphorous.