## Slide 1
Basic Electronics

## Slide 2: Electricity can be broken down into:
Electric Charge
Voltage
Current
Resistance

## Slide 3: Negative & Positive Charges
What do the effects of electricity in TV, radio, a battery, and lightening all have in common?
Basic particles of electric charge with opposite polarities.
Basic Electronics

## Slide 4: Electrons
The smallest amount of electrical charge having the quality called negative polarity.
Electrons orbit the center of atoms.
The proton is a basic particle with positive polarity.
Protons are located in the nucleus of atoms along with neutrons, particles which have neutral polarity.
Protons

## Slide 6: Electrically, all materials fall into 1 of 3 classifications:
Conductors
Insulators
Semi-Conductors

## Slide 7: Conductors
Have 1 valence electron
Materials in which electrons can move freely from atom to atom are called conductors.
In general all metals are good conductors.
The purpose of conductors is to allow electrical current to flow with minimum resistance.

## Slide 8: Insulators
Have 8 valence electrons
Materials in which electrons tend to stay put and do not flow easily from atom to atom are termed insulators.
Insulators are used to prevent the flow of electricity.
Insulating materials such as glass, rubber, or plastic are also called dielectrics, meaning they can store charges.
Dielectric materials are used in components like capacitors which must store electric charges.

## Slide 9: Semi-Conductors
Have 4 valence electrons
Materials which are neither conductors nor insulators
Common semi conductor materials are carbon, germanium and silicone.
Used in components like transistors

## Slide 10: The Symbol for Charge
The symbol for charge is Q which stands for quantity.
The practical unit of charge is called the coulomb (C).
One coulomb is equal to the amount of charge of 6.25X1018 electrons or protons stored in a dielectric.

## Slide 11: Voltage
Potential refers to the the possibility of doing work.
Any charge has the potential to do the work of attracting a similar charge or repulsing an opposite charge.
The symbol for potential difference is E (for electromotive force)
The practical unit of potential difference is the volt (V)
1 volt is a measure of the amount of work required to move 1C of charge

## Slide 12: Current
When a charge is forced to move because of a potential difference (voltage) current is produced.
In conductors - free electrons can be forced to move with relative ease, since they require little work to be moved.
So current is charge in motion.
The more electrons in motion the greater the current.

## Slide 13: Amperes
Current indicates the intensity of the electricity in motion. The symbol for current is I (for intensity) and is measured in amperes.
The definition of current is: I = Q/T
Where I is current in amperes, Q is charge in coulombs, and T is time in seconds.

## Slide 14: 1 ampere = 1 coulomb per second

## Slide 15: Resistance
Opposition to the flow of current is termed resistance.
The fact that a wire can become hot from the flow of current is evidence of resistance.
Conductors have very little resistance.
Insulators have large amounts of resistance.

## Slide 16: Ohms
The practical unit of resistance is the ohm designated by the Greek letter omega: Ω
A resistor is an electronic component designed specifically to provide resistance.

## Slide 17: Closed Circuits
In applications requiring the use of current, electrical components are arranged in the form of a circuit.
A circuit is defined as a path for current flow.

## Slide 18: Common Electronic Component Symbols

## Slide 19: A Complex Audio Circuit

## Slide 20: Open Circuits

## Slide 21: The Circuit is a Load on the Voltage Source
The circuit is where the energy of the source (battery) is carried by means of the current through the the various components.
The battery is the source, since it provides the potential energy to be used.
The circuit components are the load resistance - they determines how much current the source will produce.

## Slide 22: Direction of Electron Flow
The direction of electron flow in our circuit is from the negative side of the battery, through the load resistance, back to the positive side of the battery.
Inside the battery, electrons move to the negative terminal due to chemical action, maintaining the potential across the leads.

## Slide 23: Electron Flow in a Simple Circuit

## Slide 24: DC
Circuits that are powered by battery sources are termed direct current circuits.
This is because the battery maintains the same polarity of output voltage. The plus and minus sides remain constant.

## Slide 25: Waveform of DC Voltage

## Slide 26: Characteristics of DC
It is the flow of charges in just one direction and...
The fixed polarity of the applied voltage which are characteristics of DC circuits

## Slide 27: AC
An alternating voltage source periodically alternates or reverses in polarity.
The resulting current, therefore, periodically reverses in direction.
The power outlet in your home is 60 cycle ac - meaning the voltage polarity and current direction go through 60 cycles of reversal per second.
All audio signals are AC also.

## Slide 28: Waveform of AC Voltage

## Slide 29: Complex Voltage
This is a more realistic view of what
an audio signal’s voltage would look like

## Slide 30: Comparison of DC & AC
DC Voltage | AC Voltage
Fixed polarity | Reverses polarity
Can be steady or vary in magnitude | Varies in magnitude between reversals in polarity
Steady value cannot be stepped up or down by a transformer | Used for electrical power distribution
Electrode voltage for tube and transistor amps | I/O signal for tube and transistor amps
Easier to measure | Easier to amplify
Heating Effects the same for both AC and DC current

## Slide 31: Many Circuits Include both AC & DC Voltages
DC circuits are usually simpler than AC circuits.
However, the principles of DC circuits also apply to AC circuits.

## Slide 32: Ohm’s Law
The amount of current in a circuit is dependent on its resistance and the applied voltage. Specifically I = E/R
If you know any two of the factors E, I, and R you can calculate the third.
Current I = E/R
Voltage E = IR
Resistance R = E/I

## Slide 33: Current is Directly Proportional to Voltage for a Constant Resistance
OHM’s LAW

## Slide 34: Power
The unit of electrical power is the watt.
Power is how much work is done over time.
One watt of power is equal to the work done in one second by one volt moving one coulomb of charge. Since one coulomb a second is an ampere:
Power in watts = volts x amperes
P = E x I
P = I2 x R
P = E2 / R

## Slide 35: 3 Power Formulas
P = E x I
P = I2 x R
P = E2 / R